# Communications
The board speaks two types of protocols: text and binary. The text protocol is intended for direct human interaction such as testing. The binary protocol is intended for machine to machine communications.
The text protocol is in the CLI style. There is a series of commands. Each command takes certain parameters. One can get a list of supported commands by typing ? Followed by the Enter key in a terminal that is connected to the board.
The binary protocol is a simple request/response model. The base component is a message. A controlling device sends a message to the board and the board responds in turn with another message. Specific functionality within the board is addressable via call indexes. A call index is a unique eight bit value that identifies a function. A call index is sent as part of the request message and also as part of the response message.
Note: There are no provisions to combine binary and text protocols. This is generally not an issue with the text protocol as it doesn’t really have a state or structure. Binary protocol does have an expected message format and as such a text protocol blurb during a binary message will undoubtedly corrupt the binary message.
# Physical Connection
In order to connect to the board a serial link with CTS/RTS support is required. Most USB adapters do not support CTS/RTS flow control and thus will not work. The cable used must be standard serial null-modem cable.
# Software
The board may be accessed and controlled by any and all software that speaks RS232. For text mode communications a standard terminal program such as minicom does work. For binary mode communications the LOGIC_CORE component is the “official” implementation.
## Terminal
Representative image of a terminal session
In order to communicate using minicom, set the port to 19200 8N1. You may have to play with the line feed and the local echo settings.
## LOGIC_CORE
LOGIC_CORE is the main speaker of the binary protocol. It is the software component that contains the control logic. It is also the component that all of the HMI_SHIMs connect to.
# Binary Protocol
All multi-byte binary protocol types (for example integers) are sent down the wire with the MSB (Most Significant Byte) first. In other words, assuming a transmission of two words I1 and I2 , the receiving buffer will look like this:

Buffer index 0	Buffer index 1	Buffer index 2	Buffer index 3
I1 MSB	I1 LSB	I2 MSB	I2 LSB

NOTE: This is in contrast to the I2C protocol which sends data down the wire LSB (Least Significant Byte) first. This is a design feature and definitely not an oopsie.
The binary protocol is a simple request/response model. The controlling device sends a request and the board responds with a response.
## Request
The request message has three fields:
1. Binary message identifier (one byte)
2. Request payload length (one word)
3. Request payload (function specific)
### Binary message identifier
This is always 0x40 (ASCII @). Presence of this character indicates to the message parser on the board that the rest of the bytes are part of a binary message.
### Payload length
This is a single word value that indicates the length of the payload in bytes. Maximum payload length is 65536 bytes.
### Payload
The only standard part of the payload is the first byte which is expected to be the call index. All remaining bytes are function specific.
Request Message
Binary message identifier	Request payload length MSB
BYTE 0	BYTE 1
0x40

Request payload length LSB	Request payload
BYTE 2	BYTE 3 ...

## Response
The response message is very similar to the request message. The response message has the following fields:
1. Binary message identifier (one byte)
2. Call index (one byte)
3. Result code (one byte)
4. Response payload length (one word)
5. Response payload (function specific)
### Binary message identifier
This is always character 0x10.
### Call index
The call index that this message is in response to. This will be the same call index as in the request message.
### Result code
Function specific result code. The only standard codes are one and zero; one is success and zero is failure.
### Response payload length
Single word that indicates the length of the response payload.
### Response payload
Unlike the request payload there is no structure. The response data is function specific.
Response Message
Binary message identifier	Call index
BYTE 0	BYTE 1
0x10	Same as the call index in request

Result code.	Response payload length MSB
BYTE 2	BYTE 3
1 == success

Response payload length LSB	First byte of payload
BYTE 4	BYTE 5

NOTE: The binary message identifier is different between the request and response messages.
# Binary commands
Below is a list of supported binary commands. Some are not yet implemented and are marked as such.
## 0x00 – Reset board
Request message
Binary message identifier	Request payload length MSB
BYTE 0	BYTE 1
0x40	0x00

Request payload length LSB	Request payload byte
BYTE 2	BYTE 3
0x01	0x00

There is no response to a reset request, since the board will be resetting. A board’s reset is sensed by a protocol level log message.
## 0x01 – Get analog input values
Request message
Binary message identifier	Request payload length MSB
BYTE 0	BYTE 1
0x40	0x00

Request payload length LSB	Request payload byte
BYTE 2	BYTE 3
0x01	0x01

Response messages
Binary message identifier	Call Index
BYTE 0	BYTE 1
0x10	0x01

Result code	Response payload length MSB
BYTE 2	BYTE 3
0x01	0x00

Response payload length LSB	Response payload byte 0
BYTE 4	BYTE 5
0x10	<some value>

Response payload byte 1	Response payload byte 2
BYTE 6	BYTE 7
<some value>	<some value>
An so forth in this manner until all of the analog values are transmitted

The total payload length is 16 (0x10) because there are eight analog inputs and each analog value is 12 bits thus requiring two bytes per value.
## 0x02 – Get digital output status
Request message
Binary message identifier	Request payload length MSB
BYTE 0	BYTE 1
0x40	0x00

Request payload length LSB	Request payload byte
BYTE 0	BYTE 1
0x01	0x02

Response message
Binary message identifier	Call Index
BYTE 0	BYTE 1
0x10	0x01

Result code	Response payload length MSB
BYTE 2	BYTE 3
0x01	0x00

Response payload length LSB	Response payload byte 0
BYTE 4	BYTE 5
0x10	<output bits>

Each output state is represented by a bit. 1 means on, 0 means off. There are four digital outputs and the bottom four bits map to them. Bit 0 is output 0, bit 1 is output 1, and so forth.
## 0x03 – Set digital output status
Request message
Binary message identifier	Request payload length MSB
BYTE 0	BYTE 1
0x40	0x00

Request payload length LSB	Request payload byte 0
BYTE 1	BYTE 2
0x01	0x03

Request payload byte 1
BYTE 3
<digital output status bits>

Response message
Binary message identifier	Call Index
BYTE 0	BYTE 1
0x10	0x01

Result code	Response payload length MSB
BYTE 2	BYTE 3
0x01	0x00

Response payload length LSB	Response payload byte 0
BYTE 4	BYTE 5
0x01	0xFF

See call index 0x02 (above) for details on the status bits.
## 0x04 – Get PMIC status
Request message
Binary message identifier	Request payload length MSB
BYTE 0	BYTE 1
0x40	0x00

Request payload length LSB	Request payload byte
BYTE 0	BYTE 1
0x01	0x04

Response messages
Binary message identifier	Call Index
BYTE 0	BYTE 1
0x10	0x04

Result code	Response payload length MSB
BYTE 2	BYTE 3
0x01	0x00

Response payload length LSB	Response payload byte 0
BYTE 4	BYTE 5
0x10	<PMIC status bits>

There are two PMICs (power management IC) on the board. One protects the digital outputs from over-current condition. The other protects the analog inputs from over-current condition.
Bit 0	Analog input PMIC enabled status. 1 is enabled, 0 is disabled.
Bit 1	Digital output PMIC enabled status. 1 is enabled, 0 is disabled.
Bit 2	Analog input PMIC error status. 1 indicates error condition. 0 indicates no error condition.
Bit 3	Digital output PMIC error status. 1 indicated error condition. 0 indicates no error condition.

## 0x05 – Set PMIC status
Request message
Binary message identifier	Request payload length MSB
BYTE 0	BYTE 1
0x40	0x00

Request payload length LSB	Request payload byte
BYTE 0	BYTE 1
0x01	0x05

Request payload byte 1
BYTE 3
<digital output bits>

Response message
Binary message identifier	Call Index
BYTE 0	BYTE 1
0x10	0x01

Result code	Response payload length MSB
BYTE 2	BYTE 3
0x01	0x00

Response payload length LSB	Response payload byte 0
BYTE 4	BYTE 5
0x01	0xFF

See call index 0x04 for details on the status bits. If a PMIC is in an error state, enabling/disabling flags are ignored by the board. The error condition must first be acknowledged and reset. This is done by setting the error status bit of the faulted PMIC and invoking call index 0x05. In other words, send back the message that indicated the failure to the board.
## 0x06 – Get L1 calibration offsets
Request message
Binary message identifier	Request payload length MSB
BYTE 0	BYTE 1
0x40	0x00

Request payload length LSB	Request payload byte
BYTE 0	BYTE 1
0x01	0x06

Response messages
Binary message identifier	Call Index
BYTE 0	BYTE 1
0x10	0x06

Result code	Response payload length MSB
BYTE 2	BYTE 3
0x01	0x00

Response payload length LSB	Response payload byte 0
BYTE 4	BYTE 5
0x10	<some value>

Response payload byte 1	Response payload byte 2
BYTE 6	BYTE 7
<some value>	<some value>
An so forth in this manner until all of the calibration offsets are transmitted

The payload is a word for each analog input. This means, of course, that the payload length will always be 16 bytes. The MSB of the word is the positive offset and the LSB of the word is the negative offset. It only makes sense if either the negative or a positive offset is specified. The software stack does not enforce this though. The analog values are calculated by the board by first adding the positive calibration offset followed by subtracting the negative offset. So, for example, if both a positive and negative offset of 10 is specified, the resulting offset is zero.

## 0x07 – Get L2 calibration offsets
Request message
Binary message identifier	Request payload length MSB
BYTE 0	BYTE 1
0x40	0x00

Request payload length LSB	Request payload byte
BYTE 0	BYTE 1
0x01	0x07

Response message
See response message for 0x06 as it is identical with exception of the call index.
## 0x08 – Set L1 calibration offsets
Request message
Binary message identifier	Request payload length MSB
BYTE 0	BYTE 1
0x40	0x00

Request payload length LSB	Request payload byte 1
BYTE 0	BYTE 1
0x01	0x08

Request payload byte 2	Request payload byte 3
BYTE 2	BYTE 3
<AI0 positive offset>	<AI0 positive offset>

Request payload byte 4	Request payload byte 5
BYTE 4	BYTE 5
<AI1 positive offset>	<AI1 negative offset>
An so forth in this manner until all of the calibration offsets are transmitted

Response message
Binary message identifier	Call Index
BYTE 0	BYTE 1
0x10	0x08

Result code	Response payload length MSB
BYTE 2	BYTE 3
0x01	0x00

Response payload length LSB	Response payload byte 0
BYTE 4	BYTE 5
0x01	0xFF

## 0x09 – Set L2 calibration offsets
Request message
Binary message identifier	Request payload length MSB
BYTE 0	BYTE 1
0x40	0x00

Request payload length LSB	Request payload byte
BYTE 0	BYTE 1
0x01	0x09

Request payload byte 2	Request payload byte 3
BYTE 2	BYTE 3
<AI0 positive offset>	<AI0 positive offset>

Request payload byte 4	Request payload byte 5
BYTE 4	BYTE 5
<AI1 positive offset>	<AI1 negative offset>
An so forth in this manner until all of the calibration offsets are transmitted

Response message
See response message for call index 0x08.
## 0x0A – Get boot count
Request message
Binary message identifier	Request payload length MSB
BYTE 0	BYTE 1
0x40	0x00

Request payload length LSB	Request payload byte
BYTE 0	BYTE 1
0x01	0x0A

Response messages
Binary message identifier	Call Index
BYTE 0	BYTE 1
0x10	0x0A

Result code	Response payload length MSB
BYTE 2	BYTE 3
0x01	0x00

Response payload length LSB	Boot count MSB
BYTE 4	BYTE 5
0x02	<some value>

Boot count LSB
BYTE 6
<some value>

## 0x0B – Get board statistics
Request message
Binary message identifier	Request payload length MSB
BYTE 0	BYTE 1
0x40	0x00

Request payload length LSB	Request payload byte
BYTE 0	BYTE 1
0x01	0x0B

Response message

[ not yet implemented ]
## 0x0C – Confirm output status
Request message
Binary message identifier	Request payload length MSB
BYTE 0	BYTE 1
0x40	0x00

Request payload length LSB	Request payload byte
BYTE 0	BYTE 1
0x01	0x0C

Response message
Binary message identifier	Call Index
BYTE 0	BYTE 1
0x10	0x0C

Result code	Response payload length MSB
BYTE 2	BYTE 3
0x01	0x00

Response payload length LSB	Response payload byte 0
BYTE 4	BYTE 5
0x01	0xFF

This call index confirms that the controlling device still wants the digital outputs to remain in their current state. If a confirmation is not received within a predetermined time span the digital outputs are turned off. The motivation behind this feature is to provide a predictable failure mode in case the controlling device goes off-line unexpectedly.
For example, a Beagle Bone in conjunction with a board are controlling an A/C system. The system is in cooling mode – compressor and AHU are operational. The controlling Beagle Bone fails. The board is not aware of that and keeps the compressor and AHU operational. The result could range from space getting too cold to equipment damage due to the equipment being driven outside of its design parameters.
The requirement that the active state be confirmed on a regular basis removes that failure mode. Once the controlling device goes off-line, the board will turn the outputs off after the safety period expires.
# Text Protocol
## STATUS
### I2C
### AI
### DO
### PMIC
### B
### C
## SET
### DO
### PMIC

## COMMAND
### V
### VS
### E
## PING
## RESET
## ?